## Slide 1
19EC786
Analog VLSI design

## Slide 2
Syllabus
UNIT I BASIC MOS DEVICES 9
Depletion region of PN junction - Band diagram of MOS capacitor – Accumulation, Depletion, inversion region- Large and small signal behavior of MOSFET- short channel effects in MOS transistors – weak inversion in MOS transistors- substrate current flow in MOS transistor.
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS 9
Common source, common drain, common gate. Differential amplifiers-Cascode amplifiers-Current amplifiers–power amplifiers- Current sources and sinks ,MOS Current Mirrors – Simple, Cascode, Wilson and Widlar current source.
UNIT III CMOS OPERATIONAL AMPLIFIER 9
Design of CMOS Op amps - Compensation of Op amps- Low voltage Op amps - Low noise Op amps Two stage MOS Operational Amplifiers with Cascode, MOS Telescopic - Cascode Operational Amplifier, MOS Folded Cascode and MOS Active Cascode Operational Amplifiers.
UNITIV COMPARATORS AND SWITCHED CAPACITOR CIRCUITS 9
Characterization of a Comparator -two-Stage Open-Loop Comparators - Improving the Performance of Open-Loop Comparators-Discrete-Time Comparators - High-Speed Comparators- Switched Capacitor Circuits – Switched Capacitor Amplifiers - Switched Capacitor Integrators
UNITV A/D AND D/A CONVERTERS 9
Characterization of D/A converters- Parallel D/A converters-extending the resolution of parallel D/A converters- Serial D/A converters- Characterization of A/D converters-Serial A/D converters- Medium and high speed A/D converters.
19EC786 – Analog VLSI design

## Slide 3
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Common source, common drain, common gate.
Differential amplifiers
Cascode amplifiers
Current amplifiers
Power amplifiers
Current sources and sinks
MOS Current Mirrors
  Simple, Cascode, Wilson and Widlar current source.

## Slide 4
Single Stage Amplifiers
What aspects of the performance of an amplifier are important?
Gain, speed, power dissipation, supply voltage, linearity, noise, or maximum voltage swing, input and output impedances
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Analog design octagon

## Slide 5
Single Stage Amplifiers
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Common-Source
  Common-Source Stage with Resistive Load
  CS Stage with Diode-Connected Load
  CS Stage with Current-Source Load
  CS Stage with Triode Load
  CS Stage with Source Degeneration
Source Follower
Common-Gate Stage

## Slide 6
Common-Source Amplifier
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
A MOSFET converts variations in its gate-source voltage to a small-signal drain current, which can pass through a resistor to generate an output voltage.
The input impedance of the circuit is very high at low frequencies.
Case i: (Cut off region)
If the input voltage is Zero, M1 is Off and
Vout = VDD
Case ii: (Saturation region)
If the input voltage is Vth, M1 is ON and drawing current from RD, then
Vout = VDD - ID RD
------- (1)
------- (2)
------- (3)
Here, Channel length modulation is neglected.

## Slide 7
Common-Source Amplifier
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Further increasing Vin, then Vout decreases. The MOSFET is in saturations regions until Vin1 at point A (Fig.),
Vout = Vin1 - Vth
------- (4)
------- (5)
From (3) and (4)
Case iii: (Linear region)
------- (6)
From (2),

## Slide 8
Common-Source Amplifier
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Further increasing Vin, then Vout decreases below 2(Vin – Vth) and Vout ,
------- (7)
Small signal Gain:
From (3), Av is
------- (9)

## Slide 9
Common-Source Amplifier
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Small signal Equivalent Circuit:
From the above, Vout is,
Vout = -gmVgs (r0 || RD)
------- (10)
Since, Vin = Vgsor V1;
Av = Vout / Vin
------- (11)
------- (12)
------- (12)

## Slide 10
Common-Source Amplifier with Diode-Connected Load
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
In many CMOS technologies, it is difficult to fabricate resistors with tightly-controlled values or a reasonable physical size.
Consequently, it is desirable to replace RD with a MOS transistor.
Types of Active Loads,
CS with Diode Connected Load
CS with Current Source Load
CS with Triode Load
CS with Source Degeneration
Types of Diode Connected Loads,
CS with NMOS driver with NMOS Enhancement Load
CS with NMOS driver with PMOS Enhancement Load
CS with PMOS driver with NMOS Enhancement Load
CS with PMOS driver with PMOS Enhancement Load
CS with NMOS driver with NMOS Depletion Load
CS with NMOS driver with PMOS Depletion Load
CS with PMOS driver with NMOS Depletion Load
CS with PMOS driver with PMOS Enhancement Load

## Slide 11
Common-Source Amplifier with Diode-Connected Load
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
A MOSFET can operate as a small-signal resistor if its gate and drain are shorted.
It called a "diode-connected" device, this configuration exhibits a small-signal behavior similar to a two-terminal resistor.
The transistor is always in saturation because the drain and the gate have the same potential.
Diode-connected
NMOS and PMOS,
Small signal equivalent circuit
The impedance of the diode is simply equal to
If no Body-effect exists…

## Slide 12
Common-Source Amplifier with Diode-Connected Load
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
If Body-effect exists…
The impedance of the diode connected transistor is equal to (Apply KCL)

## Slide 13
1. CS with NMOS driver with NMOS Enhancement Load
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Load (Saturation Region)
Body effect Exists
Driver
Body effect in M2 is,
Vbs = Vb – Vs = 0 – Vs = -Vs
Equivalent circuit for Load is,
G2
D2
S2
gm2 Vgs2
gmb2 Vbs2
ro2
Vx
S1
Supply is grounded for R0 calculation. Hence, Vg2 = 0.

## Slide 14
1. CS with NMOS driver with NMOS Enhancement Load
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Applying KCL at S2 of the equivalent circuit is,
Ix + gm2 Vgs2 + gmb2 Vbs2 = Vx/ro2
------- (1)
Ix + gm2 (Vg2 - Vs2) + gmb2 (Vb2 - Vs2) = Vx/ro2
------- (2)
Using, η = gmb/ gm
Ix + gm2 (Vg2 - Vs2) + ηgm2 (Vb2 - Vs2) = Vx/ro2
------- (3)
Since Vg2 = Vb2 = 0; Vs2 = Vx
Ix – gm2 (0 - Vx) – ηgm2 (0 - Vx) = Vx/ro2
------- (4)
Ix - (Vx) (gm2 + ηgm2) = Vx/ro2
------- (5)
Ix = (Vx) (gm2 + ηgm2) +Vx/ro2
------- (6)
ROL = Vx /Ix = ro2 || (1/(gm2(1 + η))
------- (7)
Since, ro2 >> (1/(gm2(1 + η))
ROL = (1/(gm2(1 + η))
------- (8)

## Slide 15
1. CS with NMOS driver with NMOS Enhancement Load
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Equivalent circuit for Driver is,
D1
gm1 Vgs1
ro1
S1
Vin
G1
Vout
ROL
From the equivalent circuit,
Vout = - gm1 Vgs1 (ro1 || ROL)
------- (9)
Using (8) in (9),
Vout = - gm1 Vgs1 (ro1 || (1/(gm2(1 + η)))
------- (10)
Using Vgs1 = Vin in (10),
Av = Vout/Vin = - gm1 (ro1 || (1/(gm2(1 + η)))
------- (11)
Since, ro1 >> (1/(gm(1 + η)),
Av = - gm1 /(gm2(1 + η))
------- (12)
Using gm = √(2IDμnCox(W/L)) in (12),
Av = - {√(2IDμnCox(W/L)1) /((1 + η) √(2IDμnCox(W/L)2)))}
------- (13)
Av = - {√((W/L)1 /((1 + η) √(W/L)2))}
------- (14)

## Slide 16
2. CS with NMOS driver with PMOS Enhancement Load
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Equivalent circuit for Load is,
G2
D2
S2
gm2 Vgs2
ro2
S1
Vx
Vout
Vin
Vout
S2
D2
D1
S1
G2
G1
VDD
PMOS Load
(No Body Effect)
NMOS Driver
M1
M2

## Slide 17
Ix + gm2 Vsg2 = Vx/ro2
------- (1)
Ix + gm2 (Vs2 - Vg2) = Vx/ro2
------- (2)
Since Vs2 = Vb2 = 0; Vg2 = Vx
Ix + gm2 (0 - Vx) = Vx/ro2
------- (3)
Ix - (Vx) (gm2) = Vx/ro2
------- (4)
Ix = (Vx) (gm2) +Vx/ro2
------- (5)
ROL = Vx /Ix = ro2 || (1/(gm2))
------- (6)
Since, ro2 >> (1/(gm2))
ROL = (1/(gm2))
------- (7)
2. CS with NMOS driver with PMOS Enhancement Load
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Applying KCL at Vout of the equivalent circuit is,

## Slide 18
2. CS with NMOS driver with PMOS Enhancement Load
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
D1
gm1 Vgs1
ro1
S1
Vin
G1
Vout
ROL
Equivalent circuit for Driver is,
From the equivalent circuit,
Vout = - gm1 Vgs1 (ro1 || ROL)
------- (8)
Using (7) in (8),
Vout = - gm1 Vgs1 (ro1 || (1/(gm(1 + η)))
------- (9)
Using Vgs1 = Vin in (9),
Av = Vout/Vin = - gm1 (ro1 || (1/(gm2))
------- (10)
Since, ro1 >> (1/(gm(1 + η)),
Av = - gm1 /(gm2)
------- (11)
Using gm = √(2IDμnCox(W/L)) in (12),
Av = - {√(2IDμnCox(W/L)1) /( √(2IDμnCox(W/L)2))}
------- (12)
Av = - {√((W/L)1) /(√(W/L)2))}
------- (13)

## Slide 19
3. CS with PMOS driver with NMOS Enhancement Load
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Equivalent circuit for Load is,
G2
D2
S2
gm2 Vgs2
ro2
S1
Vx
Vout
Vout
S1
D1
D2
S2
G1
G2
VDD
NMOS Load
(No Body Effect)
PMOS Driver
M2
M1
Vin

## Slide 20
Ix = gm2 Vgs2 + Vx/ro2
------- (1)
Ix = gm2 (Vg2 - Vs2) + Vx/ro2
------- (2)
Since Vs2 = Vb2 = 0 (GND); Vg2 = Vx
Ix = gm2 (Vx - 0) + Vx/ro2
------- (3)
Ix = (Vx) (gm2) + Vx/ro2
------- (4)
Ix = (Vx) (gm2) +Vx/ro2
------- (5)
ROL = Vx /Ix = ro2 || (1/(gm2))
------- (6)
Since, ro2 >> (1/(gm2))
ROL = (1/(gm2))
------- (7)
Applying KCL at Vout or at D2 of the equivalent circuit is,
3. CS with PMOS driver with NMOS Enhancement Load
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS

## Slide 21
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
D1
gm1 Vgs1
ro1
S1
Vin
G1
Vout
ROL
Equivalent circuit for Driver is,
From the equivalent circuit,
Vout = - gm1 Vgs1 (ro1 || ROL)
------- (8)
Using (7) in (8),
Vout = - gm1 Vgs1 (ro1 || (1/(gm(1 + η)))
------- (9)
Using Vgs1 = Vin in (9),
Av = Vout/Vin = - gm1 (ro1 || (1/(gm2))
------- (10)
Since, ro1 >> (1/(gm(1 + η)),
Av = - gm1 /(gm2)
------- (11)
Using gm = √(2IDμnCox(W/L)) in (12),
Av = - {√(2IDμnCox(W/L)1) /( √(2IDμnCox(W/L)2))}
------- (12)
Av = - {√((W/L)1) /(√(W/L)2))}
------- (13)
3. CS with PMOS driver with NMOS Enhancement Load

## Slide 22
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
4. CS with PMOS driver with PMOS Enhancement Load
Vout
S1
D1
D2
S2
G1
G2
VDD
PMOS Load
(No Body Effect)
PMOS Driver
M2
M1
Vin
Equivalent circuit for Load is,
G2
D2
S2
gm2 Vsg2
gmb2 Vsb2
ro2
Vx
S1
Supply is grounded for R0 calculation. Hence, Vg2 = 0.

## Slide 23
Applying KCL at S2 of the equivalent circuit is,
Ix = gm2 Vsg2 + gmb2 Vsb2 + Vx/ro2
------- (1)
Ix = gm2 (Vs2 - Vg2) + gmb2 (Vs2 - Vb2) + Vx/ro2
------- (2)
Using, η = gmb/ gm
Ix = gm2 (Vs2 - Vg2) + ηgm2 (Vs2 - Vb2) - Vx/ro2
------- (3)
Since Vg2 = 0; Vs2 = Vx ; Vb2 = connected to VDD
Ix = gm2 (Vx - 0) + ηgm2 (Vx - 0) + Vx/ro2
------- (4)
Ix = (Vx) (gm2 + ηgm2) + Vx/ro2
------- (5)
Ix = (Vx) (gm2 + ηgm2) +Vx/ro2
------- (6)
ROL = Vx /Ix = ro2 || (1/(gm2(1 + η))
------- (7)
Since, ro2 >> (1/(gm2(1 + η))
ROL = (1/(gm2(1 + η))
------- (8)
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
4. CS with PMOS driver with PMOS Enhancement Load

## Slide 24
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
4. CS with PMOS driver with PMOS Enhancement Load
Equivalent circuit for Driver is,
D1
gm1 Vgs1
ro1
S1
Vin
G1
Vout
ROL
From the equivalent circuit,
Vout = gm1 Vsg1 (ro1 || ROL)
------- (9)
Using (8) in (9),
Vout = -gm1 Vsg1 (ro1 || (1/(gm2(1 + η)))
------- (10)
Using Vsg1 = 0-Vin in (10),
Av = - Vout/Vin = - gm1 (ro1 || (1/(gm2(1 + η)))
------- (11)
Since, ro1 >> (1/(gm(1 + η)),
Av = - gm1 /(gm2(1 + η))
------- (12)
Using gm = √(2IDμnCox(W/L)) in (12),
Av = - {√(2IDμnCox(W/L)1) /((1 + η) √(2IDμnCox(W/L)2)))}
------- (13)
Av = - {√((W/L)1 /((1 + η) √(W/L)2))}
------- (14)

## Slide 25
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
5. CS with PMOS driver with PMOS Depletion Load
ROL = (1/(gm2 η))
Av = - gm1 /(gm2 η)
5. CS with NMOS driver with PMOS Depletion Load
ROL = ro2
Av = - gm1 (ro1 || ro2)
6. CS with PMOS driver with NMOS Depletion Load
ROL = ro2
Av = - gm1 (ro1 || ro2)
5. CS with NMOS driver with NMOS Depletion Load
ROL = (1/(gm2 η))
Av = - gm1 /(gm2 η)

## Slide 26
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
CS with Source Degeneration
A diode-connected load provides linear behavior for CS stage.
This can be accomplished by placing a "degeneration” resistor in series with the source terminal.
“Degeneration” is just another name for negative feedback
Why is there the need of degeneration resistor in CS stage?
As the input to the gate goes more positive the current through the degeneration resistor in the source circuit increases, reducing the gate-to-source voltage slightly (Vgs=Vg-Vs). This is series negative feedback… it reduces the overall gain, increases linearity, and increases the amplifier's effective output impedance.
What is source degeneration mean?
The addition of a circuit element between a transistor source and ground, with several effects, including a reduction in gain.

## Slide 27
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
CS with Source Degeneration
G
D
S
gm Vgs
gmb Vbs
ro
Vout
Rs
Vin
RD
x
Iout
ID
Ir0
Iout
Vout
Equivalent circuit is,

## Slide 28
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
CS with Source Degeneration
From the equivalent circuit,
Vout = Voltage drop across r0 + Voltage drop across Rs.
Vout = Ir0 r0 + Iout Rs ------- (1)
Whereas,
Iout = 0 – Vout/RD ------- (2)
Sub (2) in (1), we get,
Vout = Ir0 r0 – (Vout Rs /RD) ------- (3)

## Slide 29
Ir0 + gm Vgs + gmb Vbs = Iout
------- (4)
Ir0 + gm (Vg –Vs ) + gmb (Vb - Vs) = -Vout/RD
------- (5)
Using, η = gmb/ gm; Vb = 0; Vg = Vin; Vs = -Vout Rs/RD
Ir0 + gm Vin + gm Vout Rs/RD + ηgm (0 + Vout Rs/RD) = -Vout/RD
------- (6)
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
CS with Source Degeneration
Applying KCL at node ‘x’ of the equivalent circuit is,
Ir0 = -gm Vin - gm Vout Rs/RD - ηgm ( Vout Rs/RD) -Vout/RD
------- (7)
Sub., (7) in (3),
Vout = [-gm Vin - gm Vout Rs/RD - ηgm ( Vout Rs/RD) -Vout/RD ]r0 – (Vout Rs /RD)
Vout + gm r0 Vout Rs/RD + ηgm r0( Vout Rs/RD) +Vout r0 /RD + (Vout Rs /RD) = -gm Vin r0
Vout [1+ gm r0 Rs/RD + ηgm r0(Rs/RD) + r0 /RD + (Rs /RD)] = -gm Vin r0
Av =Vout / Vin = -gm r0 / [1+ gm r0 Rs/RD + ηgm r0(Rs/RD) + r0 /RD + (Rs /RD)]
------- (8)

## Slide 30
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
CS with Source Degeneration
Drain Current and Transconductance
Without Source Degeneration
With Source Degeneration
Output Resistance:
D
S
gm Vgs
gmb Vbs
ro
Rs
RD
x
Ix
ID
Ir0
Iout
G
Vx

## Slide 31
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
CS with Source Degeneration
Ix = gm Vgs + gmb Vbs + (Vx – Vs)/r0
Vs = IxRs; r0 = Vx/Ix ; Vb = Vg =0
------- (9)
Using the above in (10) we get,
Ix = gm (Vg –Vs) + ηgm (Vb-Vs) + (Vx – Vs)/r0
------- (10)
Ix = gm (0 –IxRs) + ηgm (0 - IxRs) + (Vx – IxRs)/r0
------- (11)
Ix (1 + gm Rs + ηgm Rs + Rs/r0) =Vx/r0
------- (12)
R0 = Vx/Ix = (r0 + gm Rs r0 + ηgm r0 Rs + Rs)
R0 = Vx/Ix = (r0+ gm r0Rs (1+ η) + Rs)
------- (13)
------- (14)
Rout = RD || R0

## Slide 32
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Source Follower (Common Drain)
To achieve a high voltage gain with limited supply voltage, the load impedance must be as large as possible.
If such a stage is to drive a low-impedance load, then a "buffer" must be placed after the amplifier so as to drive the load with negligible loss of the signal level.
The source follower (also called the "common-drain" stage) can operate as a voltage buffer.
The source follower senses the signal at the gate and drives the load at the source, allowing the source potential to “follow” the gate voltage. Hence, it is called Source Follower.
When
Vin = 0, M1 is Off and Vout =0
Vin >Vth then M1 is in Saturation and Vout = Vin.
Source Follower
Input Output Characteristics
Here,
Vb ≠ Vs
ஃ body effect exists.

## Slide 33
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Source Follower (Common Drain)
G
D
S
gm Vgs
gmb Vbs
Rs
Vx
ro
The equivalent circuit is,
Source Follower

## Slide 34
Ix + gm Vgs + gmb Vbs = Vx/r0
Vs = Vx; Vb = Vg =0
------- (1)
Using the above in (2) we get,
Ix + gm (Vg –Vs) + ηgm (Vb-Vs) = Vx/r0
------- (2)
Ix + gm (0 – Vx) + ηgm (0 - Vx) = Vx/r0
------- (3)
Ix - gm Vx - ηgm Vx = Vx/r0
------- (4)
Rout = Vx/Ix = {1/((1/r0) +gm (1+ η))}
------- (6)
------- (8)
Rout = Rout || Rs= 1/(gm (1+ η)) || Rs
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Source Follower (Common Drain)
Ix = gm Vx (1+ η) + Vx/r0
------- (5)
Since, ro >> (1/(gm (1+ η)))
Rout = Vx /Ix = ro || (1/(gm (1+ η)))
Rout = Vx /Ix = 1/(gm (1+ η))
If Rs is included, then
------- (7)
The Output resistance is ,

## Slide 35
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Source Follower (Common Drain)
The Gain of the amplifier is ,
Vg = Vin;
Vs = Vout;
Vb =0;
Rs || r0
G
D
S
gm Vgs
gmb Vbs
r0
Vin
Vout
Rs

## Slide 36
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Source Follower (Common Drain)
Vout = (gm Vgs + gmb Vbs) (r0 || Rs) ------- (9)
Vout = (gm (Vg -Vs) + ηgm (Vb-Vs) (r0 || Rs) ------- (10)
Vout = (gm (Vin -Vout) + ηgm (0-Vout)) (r0 || Rs) ------- (11)
Vout = (gm Vin - gm Vout - ηgm Vout) (r0 || Rs) ------- (12)
Vout + (gm Vout + ηgm Vout) (r0 || Rs) = gm Vin (r0 || Rs)
Vout (1 +(gm + ηgm) (r0 || Rs)) = gm Vin (r0 || Rs) ------- (13)
Vout (1 +(1+ η) gm (r0 || Rs)) = gm Vin (r0 || Rs)
Av = Vout / Vin = gm (r0 || Rs) / (1 +(1+ η) gm (r0 || Rs))
------- (14)

## Slide 37
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Common Gate Amplifier
A common-gate (CG) stage senses the input at the source and produces the output at the drain.
The gate is connected to a dc voltage to establish proper operating conditions.
Note that the bias current of M1 flows through the input signal source
Alternatively, as depicted in Fig, M1 can be biased by a constant current source, with the signal capacitive coupled to the circuit.
Common-gate stage with
direct coupling at input
Common-gate stage with
capacitive coupling at input
I/O Characteristics

## Slide 38
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Common Gate Amplifier
Let us consider the common gate topology with the output impedance of the transistor and input impedance of the signal source.
CG with finite output resistance
G
D
S
gm Vgs
gmb Vbs
ro
Vout
Rs
RD
x
Iout
ID
Ir0
Iout
Vout
Vin
Vs

## Slide 39
From the equivalent circuit,
Vout = Voltage drop across r0 (Vr0) + Voltage drop across Rs (Vs).
Vout = Ir0 r0 + (Iout Rs+Vin) ------- (1)
Whereas,
Iout = 0 – Vout/RD ------- (2)
Sub (2) in (1), we get,
Vout = Ir0 r0 – (Vout Rs /RD) ------- (3)
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Common Gate Amplifier

## Slide 40
Ir0 + gm Vgs + gmb Vbs = Iout
------- (4)
Ir0 + gm (Vg –Vs ) + gmb (Vb - Vs) = -Vout/RD
------- (5)
Using, η = gmb/ gm; Vb = 0; Vg = 0; Vs = -Vout Rs/RD +Vin
Ir0 + gm (0-Vout Rs/RD +Vin) + ηgm (0 - Vout Rs/RD +Vin) = -Vout/RD
------- (6)
Ir0 = - gm (Vout Rs/RD -Vin) - ηgm (Vout Rs/RD –Vin) -Vout/RD
------- (7)
Sub., (7) in (3),
Vout = [- gm (Vout Rs/RD -Vin) - ηgm (Vout Rs/RD –Vin) -Vout/RD]r0 – Vout Rs /RD +Vin
Vout + r0 Vout /RD + ηgm r0( Vout Rs/RD) + gm r0( Vout Rs/RD) + (Vout Rs /RD) = Vin + Vin r0 gm + Vin r0 η gm
Vout [1+ gm r0 Rs/RD + ηgm r0(Rs/RD) + r0 /RD + (Rs /RD)] = Vin [1+ gm r0 + ηgm r0]
Av =Vout / Vin = [1+ gm r0 + ηgm r0] / [1+ gm r0 Rs/RD + ηgm r0(Rs/RD) + r0 /RD + (Rs /RD)]
Av =Vout / Vin = RD[1+ gm r0 (1 + η)] / [RD+ gm (1 + η)gm r0Rs + r0 + Rs)]
------- (8)
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Common Gate Amplifier
Applying KCL at node ‘Vout’ of the equivalent circuit is,

## Slide 41
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Common Gate Amplifier
Output Resistance:
D
S
gm Vgs
gmb Vbs
ro
Rs
RD
x
Ix
ID
Ir0
Iout
G
Vx
VS

## Slide 42
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Common Gate Amplifier
Ix = gm Vgs + gmb Vbs + (Vx – Vs)/r0
Vs = IxRs; R0 = Vx/Ix ; Vb = Vg =0
------- (9)
Using the above in (10) we get,
Ix = gm (Vg –Vs) + ηgm (Vb-Vs) + (Vx – Vs)/r0
------- (10)
Ix = gm (0 –IxRs) + ηgm (0 - IxRs) + (Vx – IxRs)/r0
------- (11)
Ix (1 + gm Rs + ηgm Rs + Rs/r0) =Vx/r0
------- (12)
R0 = Vx/Ix = (r0 + gm Rs r0 + ηgm r0 Rs + Rs)
R0 = Vx/Ix = (r0+ gm r0Rs (1+ η) + Rs)
------- (13)
------- (14)
Rout = RD || R0
Applying KCL at node X,

## Slide 43
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Cascode Stage Amplifier
Common Gate: The input signal of a common-gate stage may be a current.
Common-source: a common-source arrangement converts a voltage signal to a current signal.
Cascode Stage: The cascade of a CS stage and a CG stage is called a "cascode"' topology.
M1 generates a small-signal drain current proportional to &, and M2 simply routes the current to RD.
M1 the input device and M2 the cascode device.
M1 and M2 carry equal currents.
The bias conditions of the cascode,
For M1 to operate in saturation, Vx > Vin -VTH1.
If M1 and M2 are both in saturation, then Vx is
Vx = Vb – VGS2.
Thus, Vb – VGS2 > Vin -VTH1.
Hence, Vb – VGS2 > Vin -VTH1 + VGS2
For M2 to be in saturation,
  Vout >Vb – VTH2 ;
  Vout> Vin -VTH1 + VGS2 – VTH2
The term cascode is believed to be the acronym for "cascaded triodes"

## Slide 44
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Cascode Stage Amplifier
The minimum output level for which both transistoors operate in saturation is equal to the overdrive voltage of M1 +M2.
That is, addition of M2 to the circuit reduces the output voltage swing by at least the overdrive voltage of M2.
It means, M2 is “Stacked” on top of M1.
I/O Characteristics
When, Vin < Vth1; then both M1 and M2 are Off; Vout = VDD & Vx =Vb – Vth2
Vin> Vth1; then M1 draws current, and Vout drops.
Since ID2 increases, VGS2 increases and Vx falls down.
When, Vin is large then,
Vx drops below Vin by Vth1 forcing M1 into Triode Region (Vx < Vin – Vth1).
Vout drops below Vb by Vth2, driving M2 into the Triode Region (Vout < Vi – Vth2).

## Slide 45
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Cascode Stage Amplifier
Output Resistance:
Vs2 = Ixro1
D2
gm2 Vgs2
gmb2 Vbs2
ro2
r01
x
Ix
Ir0
Iout
G2
Vx
G1
gm1 Vgs1
S2
D1
S1

## Slide 46
Ix = gm2 Vgs2 + gmb2 Vbs2 + (Vx – Vs2)/ro2
Vs2 = Ixro1; R0 = Vx/Ix ; Vb2 = Vg2 =0
------- (1)
Using the above in (2) we get,
Ix = gm2 (Vg2 –Vs2) + ηgm (Vb2-Vs2) + (Vx – Vs2)/ro2
------- (2)
Ix = gm2 (0 – Ixro1) + ηgm (0 - Ixro1) + (Vx – Ixro1)/ro2
Ix + gm2Ixro1 + ηgmIxro1 + Ixro1/r02 = Vx/ro2
------- (3)
Ix (1 + gm2 ro1 + ηgm ro1 + ro1/r02) =Vx/ro2
------- (4)
R0 = Vx/Ix = (1 + gm2 ro1 + ηgm ro1 + ro1/ro2) ro2
R0 = Vx/Ix = (ro2 + gm2 ro1 ro2 + ηgm ro1 ro2 + ro1)
------- (5)
------- (6)
Rout = RD || R0
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Cascode Stage Amplifier
------- (7)
------- (8)
Applying KCL at node X,

## Slide 47
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Cascode Stage Amplifier
Voltage Gain:
D2
S2
gm2 Vgs2
gmb2 Vbs2
ro2
r01
x
Iout
Ir0
Iout
G2
G1
gm1 Vgs1
Vin
D1
S1
Vout
Vg2 = 0;
Vg1 = Vin;
Vs1 = 0;
Vs2 = (Iout – gm1Vgs1)ro1
Vs2 = (-(Vout/RD) – gm1 (Vg1 –Vs1))ro1
Vs2 = (-(Vout/RD) – gm1 Vin)ro1

## Slide 48
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Cascode Stage Amplifier
Vout = Voltage drop across r01 (Vr01) + Voltage drop across r02 (Vr02).
Vout = [(-Vout/RD) - (gm2 Vgs2 + gmb2 Vbs2)] ro2 + [(-Vout/RD) - (gm1 Vgs1)] ro1 ------- (9)
Vout = [(-Vout/RD) ro2 - gm2 Vgs2 ro2 - gmb2 Vbs2 ro2] + [-(Vout ro1 /RD) - (gm1 Vgs1) ro1] ------- (10)
Vout = [(-Vout/RD) ro2 - gm2 ro2 [0-(-(Vout/RD) – gm1 Vin)ro1]- η gm2 ro2(-(Vout/RD) – gm1 Vin)ro1] +
[-(Vout ro1 /RD) - (gm1 Vin) ro1] ------- (11)
Vout+(Vout/RD) ro2 + gm2 ro1 ro2 (Vout/RD) + (Vout ro1 /RD) + η gm2 ro1 ro2(Vout/RD) =
- gm2 ro2 gm1 Vinro1 - η gm2 ro2 gm1 Vinro1 - (gm1 Vin) ro1 ------- (12)
Vout [1 + (ro2/RD) + (gm2 ro1 ro2 /RD) + (ro1 /RD) + (η gm2 ro1 ro2/RD)] =
-Vin [gm2 ro2 gm1 ro1 + η gm2 ro2 gm1 ro1 + gm1 ro1] ------- (13)
Av =Vout / Vin = - [gm1 ro1 [1+ gm2 ro2 (1 + η)]]RD / [RD + ro2 + ro1 + (gm2 ro1 ro2) (1+ η)]
------- (14)

## Slide 49
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Differential Amplifier
A differential amplifier the output signal generally is the amplified version of the difference of two inputs of the amplifier.
A source-coupled circuit as a differential voltage-to-current converter and then deal with the CMOS differential amplifier in which a current mirror circuit is employed as an active load for the source-coupled pair.
A single-ended output differential amplifier can be implemented by putting a PMOS current mirror on top of the differential amplifier.
Differential amplifier with differential input.

## Slide 50
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Differential Amplifier
In this circuit, (M1, M2) and also (M3, M4) are mutually identical with each other and thus the tail current I0 is equally divided between M1 (M3) and M2 (M4) in the absence of differential input voltage.
When vi rises, due to the positive voltage gain of the amplifier, the output voltage with a steep positive slope goes up and M4 quickly approaches the triode region where the voltage gain starts dropping.
This occurs for a rather low positive change in vi. After M4 enters the triode region, with more increase in vi, the output voltage vo continues to rise with a lower rate. At the same time the tail current steers toward M1 and the current of M2 and M4 approaches zero.
Differential amplifier drain currents versus input.

## Slide 51
When differential input voltage reaches √2I0/β, the entire tail current flows through M1 and thus M2 turns off. At this point, M4 is in triode with zero drain current, which means the drain-source voltage of M4 is zero and thus the output voltage is fixed on VDD.
When input voltage changes in the negative direction, the output voltage rapidly drops again due to the differential amplifier voltage gain and this time M2 goes to the triode region.
As long as the tail transistor operates in saturation, M5 acts as a current source, and M3 with a diode connection structure always remains in saturation.
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Differential Amplifier
On the other hand, if the source-to-drain voltage of M4 is more than VSD,sat, it will operate in saturation and the current mirror consisting of M3 and M4 forces M1 and M2 to have the same current even though M2 is in triode and therefore the drain currents of M1 and M2 remain on I0/2.
For large negative differential input voltage the tail transistor ultimately enters the triode region where the tail current starts decreasing with the input. As a result, the drain currents of M1 and M2 also decrease in parallel with each other.
Large-signal characteristic of differential amplifier

## Slide 52
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Differential Amplifier
Now let us select a widely used load consisting of a p-channel current mirror.
Under quiescent conditions (no applied differential signal, i.e., VID = 0 V), the two currents in Ml and M2 are equal and sum to Iss. the current in the current sink, M5.
The current of M1 will determine the current in M3. Ideally, this current will be mirrored in M4.
If VGS1 = VGS2 and M1 and M2 are matched. then the currents in M l and M2 are equal.
Thus, the current that M4 sources to M2 should be equal to the current that M2 requires, causing iOUT to be zero-provided that the load is negligible.
If these currents are not equal as in the following analysis, we assume that because the external load resistance is infinite that the current flows in the self-resistance of M2 and M4 (due to the channel modulation effect).
H VGS1 = VGS2 then iD1 increases with respect to iD2 since Iss = iD1 + iD2. This increase in iD1 implies an increase in iD3 and iD4.
However, iD2 decreases when VGS1 is greater than VGS2 Therefore, the only way to establish circuit equilibrium is for iOUT to become positive and VOUT to increase.
It can be seen that if VGS1 < VGS2 then iOUT becomes negative and VOUT decreases.
This configuration provides a simple way in which the differential output signal of the differential amplifier can be converted back to a single-ended signal, that is, one referenced to ac ground.

## Slide 53
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Differential Amplifier – Small Signal Analysis
D1, D3, G3, G4
S2
gm1 Vgs1
ro1
G1
gm4Vgs4
Vd/2
1/gm3
ro3
gm2Vgs2
ro4
ro2
Vd/2
D2, D4
G2
Small Signal Equivalent Circuit

## Slide 54
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Differential Amplifier – Small Signal Analysis
Small Signal Equivalent Circuit of M3,
G3
S3
gm1 Vgs1
ro3
Vx
D3
Ix
Ix = gm3 Vgs3 + Vx/ro3 ------- (1)
Ix = gm3 (Vg3 – Vs3) + Vx/ro3
Ix = gm3 (Vx – 0) + Vx/ro3
Ix = gm3 Vx + Vx/ro3
ROL = Vx /Ix = 1/(gm3 || (1/ro3)) ------- (2)
------- (14)
Applying KCL,
Vg = Vx; Vs3 = 0
ROL = Vx /Ix = 1/gm3 ------- (3)
VOUT1 = VD1 = VD3 = VG3 = VG4
VOUT1 = gm3 Vgs3 (ro1 || ro3 || (1/gm3))
VOUT1 = gm3 (Vd/2) (1/gm3) ------- (4)

## Slide 55
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Differential Amplifier – Small Signal Analysis
Io = i4 - i2 ------- (5)
Io = gm4 Vgs4 – gm2 Vgs2 ------- (6)
Io = gm4 (Vg4 – Vs4) – gm2 (Vg2 – Vs2)
Io = gm4 ((gm1Vd)/(2gm3) – 0) – gm2 (-Vd/2 – 0)
Io = (( gm4 gm1Vd)/(2gm3)) + gm2 Vd/2
Io = (( gm4 gm1Vd)/(2gm3)) + gm2 Vd/2 (for identical transistors gm1 = gm2 = gm3 = gm4)
Io = (gm4 Vd/2)+ (gm2 Vd/2)
Io = (gm4 + gm2) (Vd/2) ------- (7)
Io = gmVd ------- (8)
Output Resistance,
Rout = (ro2 || ro4)
Gain Ad = gm Rout = gm (ro2 || ro4)

## Slide 56
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Differential Amplifier – Common Mode Analysis
Vicm = Vc = Common Mode Signal

## Slide 57
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Differential Amplifier – Common Mode Analysis
D1, D3, G3, G4
S1
gmb2Vbs2
ro1
G1
gm4Vgs4
Vc
1/gm3
ro3
gm2Vgs2
ro4
ro2
D2, D4
G2
gm1Vgs1
2Rss
2Rss
Vo2
Vo1
Vc
gmb1Vbs1

## Slide 58
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Differential Amplifier – Common Mode Analysis
Vout = (i4 – i2) ro4 ------- (9)
i4 = gm4 Vgs4 = gm4 (Vg4 – Vs4) = gm4 Vg4 ------- (10)
Vg4 = i1 (ro3 || (1/gm3)) ------- (11)
Sub. (11) in (10) => i4 = gm4 i1 (ro3 || (1/gm3)) ------- (12)
Sub. (12) in (9) => Vout = ((gm4 i1 (ro3 || (1/gm3)) – i2) ro4 ------- (13)
Vc = Vgs + (i1)(2Rss)
Vgs << (i1)(2Rss)  i1 = i2 = Vc / 2Rss ------- (14)

## Slide 59
Sub. (14) in (13),
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Differential Amplifier – Common Mode Analysis
Vout = ((gm4 (Vc /2Rss) (ro3 || (1/gm3)) – (Vc /2Rss)) ro4 ------- (15)
Vout = (Vc /2Rss) ((gm4 (ro3 || (1/gm3)) – 1) ro4 ------- (16)
Vout = (Vc /2Rss) ((gm4 ro3 /(1+gm3 ro3)) – 1) ro4
Vout = (Vc ro4/2Rss) (– 1/(1+gm3 ro3)) ------- (17)
Approximately,
Vout = (Vc ro4/2Rss) (– 1/(gm3 ro3)) ------- (18)
Since all transistors are identical, ro3 = ro4,
Hence (18) becomes,
Vout = (-Vc /2Rssgm3) ------- (19)
Ac = Vout / Vc = (-1 /2Rssgm) ------- (20)

## Slide 60
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Differential Amplifier – CMRR
CMRR = |Ad| / |Ac| ------- (21)
CMRR = |gm (ro2 || ro4)| / |(-1 /2Rssgm)| ------- (22)
(ஃ ro2 = ro2 = ro)
CMRR = gm2 ro 2Rss ------- (23)

## Slide 61
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Current Mirror
Current mirrors made by using active devices have come to be widely used in analog integrated circuits both as biasing elements and as load devices for amplifier stages.
Current mirrors are frequently more economical than resistors in terms of the die area required to provide bias current of a certain value, particularly when the required value of bias current is small.
When used as a load element in transistor amplifiers, the high incremental resistance of the current mirror results in high voltage gain at low power supply voltages.
A current mirror is an element with at least three terminals, the common terminal is connected to a power supply, and the input current source is connected to the input terminal.
Ideally, the output current is equal to the input current multiplied by a desired current gain.
If the gain is unity, the input current is reflected to the output, leading to the name current mirror.
Under ideal conditions,
The current-mirror gain is independent of input frequency.
The output current is independent of the voltage between the output and common terminals (Vds).
The voltage between the input and common terminals is ideally zero because this condition allows the entire supply voltage to appear across the input current source.

## Slide 62
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Current Mirror
Deviations from ideality are,
The variation of the current-mirror output current with changes in voltage at the output terminal. This effected by the small-signal output resistance, Ro, of the current mirror. A Norton-equivalent model includes Ro in parallel with a current source controlled by the input current.
Gain error, which is the deviation of the gain of a current mirror from its ideal value. The gain error is separated into two parts: (1) The systematic gain error and (2) The random gain error. The systematic gain error, , is the gain error that arises even when all matched elements in the mirror are perfectly matched and will be calculated for each of the current mirrors. The random gain error is the gain error caused by unintended mismatches between matched elements.
When the input current source is connected to the input terminal of a real current mirror, it creates a positive voltage drop, VIN, that reduces the voltage available across the input current source. Minimizing VIN is important because it simplifies the design of the input current source, especially in low-supply applications.
A positive output voltage, VOUT, is required in practice to make the output current depend mainly on the input current. This characteristic is summarized by the minimum voltage across the output branch, VOUT(min), that allows the output device(s) to operate in the active region. Minimizing VOUT(min) maximizes the range of output voltages for which the current-mirror output resistance is almost constant.

## Slide 63
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Current Mirror
Ground referenced Current-mirror
Positive supply referenced Current-mirror

## Slide 64
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
Current Mirror
Types of Current mirrors are,
    Simple Current Mirror
    Cascode Current Mirror
    Wilson Current Mirror
    Widlar Current Mirror
Difference between Current Source and Current Mirror,
Current Source:
Output current depends on input current and independent on R0 and Vout.
Iout = Iin
Current Mirror:
Output current independent of Vcc and Temperature variations.
Iout controlled b Vgs2 (Vgs2 = Vgs1)

## Slide 65
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
1. Simple Current Mirror
The drain-gate voltage of M1 is zero; therefore, the channel does not exist at the drain, and the transistor operates in the saturation or active region if the threshold is positive.
Although the principle of operation for MOS transistors does not involve forward biasing any diodes, M1 is said to be diode connected.
Assume that M2 also operates in the active region and that both transistors have infinite output resistance.
Then ID2 is controlled by VGS2, which is equal to VGS1.

## Slide 66
The gate-source voltage of a given MOS transistor is usually separated into two parts:
The threshold Vt and the overdrive Vov.
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
1. Simple Current Mirror
------- (1)
------- (2)
Equation (2) shows that the overdrive of M2 is equal to that of M1.
If the transistors are identical, (W/L)2 = (W/L)1, and therefore (2) is,
------- (3)
------- (4)

## Slide 67
In practice, the devices need not be identical.
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
1. Simple Current Mirror
------- (5)
The output resistance of the current mirror at any given operating point is the reciprocal of the slope of the output characteristic at that point.
The point where VDS2 = VDS1 and VGS2 = VGS1 is labeled on the characteristic.
------- (6)

## Slide 68
2. For the simple MOS current mirror, the input voltage is
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
1. Simple Current Mirror
1. The systematic gain error, ε of the current mirror can be calculated
Example:
If the drain-source voltage of M1 (Vds1) is held at 1.2V, and if the drain-source voltage of M2 (Vds2) is 5 V, then the systematic gain error is (5 − 1.2)/10 = 0.38 with VA = 10 V.
3. Finally, the minimum output voltage required to keep M2 in the active region is
------- (7)
------- (8)
------- (9)

## Slide 69
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
2. Cascode Current Mirror
Cascode current mirror
I-V characteristics

## Slide 70
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
2. Cascode Current Mirror
Assume that all the transistors are identical. (M1 = M2 = M3 = M4)
β is infinite.
VGS1 = VGS2 = VGS3 = VGS4
W.K.T.,
Also, ID3 = ID4 = ID2 = ID1
And IIN = ID4 + IG4 + IG2
since IG = 0;  IIN = ID4
Similarly, IS4 = ID3 + IG1 + IG3
since IG = 0;  IS4 = ID3 ;  IS4 = IIN
IOUT = IIN = ID4
Hence,

## Slide 71
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
2. Cascode Current Mirror
D4, G2, G4
Vin
S4 = G3
gm4Vgs4
rds4
gm3Vgs3
rds3
rds2
rds1
gm2Vgs2
gm1Vgs1
Vout
Iout
S3
S1
S2
D1
D2

## Slide 72
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
2. Cascode Current Mirror
Vout = rds2 (iout – gm2 Vgs2) + rds1 (iout – gm1 Vgs1)
Vgs2 = Vg2 – Vs2 (Vg2 = 0)
Vgs2 = 0 – Vs2 = - iout rds2
Vgs1 = 0 (Diode Connected; so, Vg1 = 0 & Vs1 = 0)
Vout = rds2 (iout + gm2 iout rds2) + rds1 iout
Vout = iout (rds2 + gm2 rds22 + rds1)
Rout = Vout / iout = rds2 (1+ gm2 rds2 + rds1)
The input voltage of the MOS cascode current mirror is,
VIN = VGS3 + VGS4 (Drop across M3 & M4)
VIN = Vt3 + Vov3 + Vt4 + Vov4
(ஃVgs – Vt = Vov; Vgs = Vt + Vov)
VIN = 2Vt + 2Vov (All transistors are identical)
The minimum output voltage for which M1 and M2 operate in the active region is,
VOUT(min) = VDS1 + VDS2 (Drop across M1 & M2)
VDS1 = VGS3 = VDS3
VDS2 = Vov2 (M2 is in active region)
VOUT(min) = VGS3 + Vov2
VOUT(min) = Vov3 + Vt3 + Vov2
VOUT(min) = 2Vov + Vt

## Slide 73
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
3. Wilson Current Mirror
Assume that all the transistors are identical. (M1 = M2 = M3)
IIN = ID1 = IOUT = ID3 = IS3
G3, D1
gm1Vgs1
ro1
ro3
gmb3Vgs3
1/gm2
Vx
Ix
S3
S1
S3, G2, G1, D2
gm3Vgs3
Ix

## Slide 74
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
3. Wilson Current Mirror
Vx = Ix / gm2 + (Ix – gm3 Vgs3)ro3 + gmb3 Vbs3 ro3 ------- (1)
Vx = Ix / gm2 + Ixro3 – gm3 (Vg3 – Vs3)ro3 + gmb3 (Vb3 – Vs3) ro3 ------- (2)
Here, Vg3 = - gm1 Vgs1 ro1 (G3 is connected to D1 of M1)
Vb = 0; Vs1 = 0 (Bulk and Substrate connected to Ground)
Vg1 = Vgs2 (Gate of M1 and M2 connected together)
So, Vg3 = - gm1 Vgs2 ro1
Vs3 = Vg2 = Ix / gm2 (Source of M3 and Gate of M2 is connected)
Vg3 = - gm1 ro1 Ix / gm2
Sub., above in (2),
Vx = Ix / gm2 + Ixro3 – gm3 (- gm1 ro1 Ix / gm2 – (Ix / gm2))ro3 + gmb3 ro3 (Ix / gm2) ------- (3)
Vx = Ix [1/ gm2 + ro3 + gm3 ro3 gm1 ro1 / gm2 + gm3 ro3 / gm2 + gmb3 ro3 / gm2] ------- (4)
Vx = Ix [1/ gm2 + ro3 [1 + gm3 gm1 ro1 / gm2 + gm3 / gm2 +η gm3 / gm2]] ------- (5)
R0 = Vx / Ix = [1/ gm2 + ro3 [1 + gm3 gm1 ro1 / gm2 + gm3 / gm2 +η gm3 / gm2]] ------- (6)
R0 = Vx / Ix = [gm3 gm1 ro1 ro3 / gm2]

## Slide 75
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
3. Wilson Current Mirror
Output Resistance:
R0 = Vx / Ix = [gm3 gm1 ro1 ro3 / gm2]
Input Voltage:
Vin = VDS1 = VGS2 + VGS3 = Vt + Vov + Vt + Vov = 2 Vt + 2Vov
Output Voltage:
VOUT = VDS3 + VDS2 = VDS3 + VGS2 = Vov + Vt + Vov = Vt + 2Vov

## Slide 76
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
4. Widlar Current Mirror
If IIN > 0, M1 operates in the active region because it is diode connected. Assume that M2 also operates in the forward active region.
Vgs1 = Vgs2 + Is2R2
ID2 = Is2 = IOUT
Vgs1 = Vgs2 + IOUT R2
Vt + Vov1 = Vt + Vov2 + IOUT R2
Vov1 - Vov2 - IOUT R2 = 0
IOUT = (Vov1 - Vov2) / R2 ------- (9)
(OR)
Vov2 - Vov1 + IOUT R2 = 0 ------- (10)

## Slide 77
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
4. Widlar Current Mirror
Use above in (10),
------- (11)
(11) is similar to ax2+bx+c = 0
------- (12)

## Slide 78
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
4. Widlar Current Mirror
G1, D1
ro1
ro2
gmb2Vgs2
R2
Vx
Ix
S1
S2
D2
gm2Vgs2
Ix
1/gm
R1

## Slide 79
Ix = gm2 Vgs2 + gmb2 Vbs2 + (Vx – Vs2)/ro2 ------- (1)
Ix = gm2 (Vg2 – Vs2) + ηgm2 (Vb2 – Vs2) + (Vx – IxR2)/ro2 ------- (2)
Vgs2 = (Vg2 – Vs2) = (0 – IxR2) (Vg2 =0; Diode Connected)
Vbs2 = (Vb2 – Vs2) = (0 – IxR2) (Vb2 =0; Connected to GND)
From (2)
Ix = gm2 (0 – IxR2) + ηgm2 (0 – IxR2) + (Vx – IxR2)/ro2 ------- (3)
Ix = – gm2 IxR2 – ηgm2 IxR2 + Vx/ro2 – IxR2/ro2 ------- (4)
Ix + gm2 IxR2 + ηgm2 IxR2 + IxR2/ro2 = Vx/ro2 ------- (5)
Vx/Ix = ro2 [1+gm2 R2 + ηgm2 R2 + R2/ro2] ------- (6)
Vx/Ix = ro2 [1+(1+η)gm2 R2 + R2/ro2] ------- (7)
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
4. Widlar Current Mirror

## Slide 80
UNIT II HIGH FREQUENCY CMOS AMPLIFIERS AND CURRENT MIRROR CIRCUITS
4. Widlar Current Mirror
Output Resistance:
R0 = Vx / Ix = ro2 + (1+η)gm2 ro2 R2 + R2
R0 = Vx / Ix = ro2 [(1+η)gm2 R2]
Input Voltage:
Vin = VGS = Vt + Vov
Output Voltage:
VOUT = VDS2 + VS = Vov2 + VS